## Slide 1: Gesture Recognition
Sriram Raju Dandu

## Slide 2: Pre-requisites
Android studio
Microsoft band
Android phone
USB cable (Phone - laptop)
Code (Available on collab)

## Slide 3: What is gesture recognition?
Definition- “Mathematical interpretation of a human motion by a computing device.”
Purpose- To use simple gestures to control or interact with devices without physically touching them.
Gesture recognition can be seen as a way for computers to begin to understand human body language, thus building a richer bridge between machines and humans than primitive text user interfaces or even GUIs (graphical user interfaces), which still limit the majority of input to keyboard and mouse.

## Slide 4: Applications
Virtual/augmented environment
Gaming
Accessibility for the physically-challenged
Consumer electronics
Notes: Sensors – Camera, accel, gyroscope
Gaming – Nintendo V
Blind
Samsung screen shot

## Slide 5: Accelerometer vs Gyroscope
Linear acceleration
Relative to gravity
Low SNR
Linear motion
Angular velocity
No absolute reference
High SNR
Rotation

## Slide 6: Task 1
Identify the 6 different motions:
  Moving right
  Moving left
  Moving up
  Moving down
  Rotate clockwise
  Rotate anti-clockwise
Notes: NOTE: Watch orientation

## Slide 7: To-Do
Use accelerometer/ gyroscope axis
Choose a threshold/s for each motion

## Slide 9
Just right

## Slide 10: Task 2
Count the number of steps
Down
Idle
Up
One step

## Slide 11: Hint
If previous motion was idle, and the current one is either “Up” or “Down” then increment the step count by 0.5